Solar Sail Trajectories to the Planets

John Clouse

Most interplanetary spacecraft have used finite burns to escape Earth orbit and be captured by their destination's gravity. The propellant expended for these maneuvers is a large part of the mass and cost for these missions. If the hyperbolic excess velocity at departure and/or arrival could be reduced, propellant mass could be saved. Solar sails are an attractive technology to potentially lessen propellant expenditure. Solar sails convert solar photon momentum to spacecraft acceleration, providing a free – and potentially continuous – propulsion source. This propulsion system is only limited by sail size, reflective parameters, and orientation to the sun. This project will seek to determine the savings in hyperbolic excess velocity at departure and arrival for a baseline spacecraft and steering angle.

Bibliography

1. Stevens, R., Ross, I.M., and Matousek, S, “Earth-Mars Return Trajectories Using Solar Sails,” 55th International Astronautical Congress 2004, IAC-04-A.2.08, Vancouver, Canada, 2004.
2. Vallado, D, “Continuous-Thrust Transfers,” Fundamentals of Astrodynamics and Applications, 4th ed., The Space Technology Library, Hawthorne, CA, 2013, pp. 371-388.
3. McInnes, C., Solar Sailing: Technology, Dynamics, and Mission Applications, Springer, 2004.

Solar Sails

Solar sails use solar photon momentum to accelerate the spacecraft. The solar flux has an inverse-square relationship to the distance from the sun, just like gravitation. Therefore, the maximum acceleration provided by the sail and the acceleration due to solar gravity can form the ratio β[ROSS].

Beta =	EQN 1

The relationship in Eqn 1 provides the mission designer the ability to design trajectories without prior knowledge of spacecraft mass, sail area, and sail reflective parameters. It also allows the acceleration due to solar radiation pressure be expressed in terms of gravitational acceleration [McInnes].

The angle between the sun vector and the sail-normal vector is called the coning angle, α. This parameter is steered to produce the sailforce in the desired direction. However, it is not optimal to just steer to the coning angle between 0 and π/2 . Take the sail force direction:

EQN 2

and the vector that maximum sail force is to be applied:

EQN 3
The force magnitude f<sub>q</sub> is [McInnes]

EQN 4

By combining Eqns 2-4 and setting the result's derivative equal to zero, the optimal coning angle is found in the following expression:

EQN 5

The cone angle is shown against the desired force angle in FIGURE. Due to the transverse force component being limited by the product of sinα and cosα , one can see that maximizing the force in the transverse direction (with respect to the Sun) requires a coning angle of 35.25<sup>○</sup>

The 2D polar equations of motion for a large gravitating body and solar radiation pressure are given by [McInnes]:

EQN 2
EQN 3

From Eqns 2 and 3, it is evident that α provides no sail force at π/2.

 Optimal Trajectories