ACS
Planned Maneuvers
The planned maneuvers are simple: detumble, nominal nadir pointing, maneuver slews, and maneuver maintanance.

ACS System Description
The ACS will rely on TBD magnetic torquers to arrest rates and perform slew maneuvers. Nadir pointing will be primarily maintained by utilizing the gravity-gradient torque present due to the mass properties; the magnetic torquers will provide additional actuation as needed.

Expected Disturbance Torques
The disturbance torques expected throughout the mission are shown in Table TBD.

ACS Components
ACS components are shown in table TBD.

Mission Design
Initial velocity changes (dV) will be provided by the orbit-insertion stage of the launch vehicle. Each launcher will provide the propulsion to reach the target altitude and plane, as well as placing the satellites in conjunction in their orbit planes. Table TBD shows the range of expected dV the launch vehicle stages will be expected to accomplish.

System Overview
Mission Sequence
The Pegasus satellites will be launched as secondary payloads on three launch vehicles servicing polar orbits. The orbit stages of the launchers will have restart capability. Two satellites will be secured to an EELV Secondary Payload Adapter (ESPA). After the orbit stage successfully releases the primary payload, it will phase into the desired longitude of the ascending node using nodal recession, then change the orbit inclination to 90 degrees. The orbit stage will release one Pegasus satellite, and then lower the perigee to put the released satellite in conjunction at the tenth revolution since the maneuver. The orbit stage will then recircularize at 600 km altitude and release the second satellite. This process will be repeated for the other two launches, and the orbit planes will be 30 degrees apart.

After each Pegasus satellite is released, the attitude control system (ACS) will arrest rates and orient the antennas and instruments nadir. The satellites are expected to maintain pointing with the use of passive and active techniques for the rest of their operational lifetimes. (TODO: do we need to reposition for station keeping?? Collision avoidance?)

The Pegasus system shall be comprised of at least six satellites.
Each Pegasus satellite shall collect data from ground stations.
Each Pegasus satellite shall carry an earth observation payload.
The Pegasus system shall provide ROI within three years.
The Pegasus satellites shall have a lifetime of two years.
The Pegasus satellites shall be autonomous for quiescent operations
maintenance